## Slide 1: Unmanned System health management
邱江杰, 胡天祁, 姚润徽
2024/01/02

## Slide 2: TABLE OF CONTENT
Background Introduction
Data Pre-Processing
Methods and Results
Conclusion and Discussion

## Slide 3: Background Introduction
Motivation: intelligent unmanned systems perform tasks in a complex and unknown environment  failures or anomalies can result in severe accidents  fault diagnosis capabilities essential for ensuring safety and reliability
Small quadrotor autonomous underwater vehicle (AUV):
  investigate and monitor the environment of inland waters (e.g., lakes, reservoirs)
  five health conditions: normal state (F1), abnormal load (F2), depth sensor failure (F3), major propeller failure (F4), and minor propeller failure (F5).
Dataset: 16 different sensors (motor control signals, battery voltage, depth, angular velocity, acceleration, and vehicle attitude information) with 250 data samples for each health conditions  1220 data samples
Goal: A classification algorithm to identify AUV fault situations

## Slide 4: Data pre-Processing
Normalization
  Max Scaling
  Min-Max Scaling
Data Augmentation
  Sliding Window Data Augmentation
Anomaly Detection
  Isolation Forest Algorithm
Shuffle Data
One-Hot Encoding

## Slide 5: Methods and results
First approach by implementing popular algorithms for classification of time series data
Algorithm | Accuracy
Decision Tree | 87.8%
Random Forest | 96.7%
Support Vector Machine: | 88.6%
Bagging | 93.9%
CNN (1 Conv Layer) | 72.2%
CNN (2 Conv Layer) | 80.8%
RNN | 80.0%

## Slide 6: Methods and results - Random Forest
Meta estimator that fits a number of decision tree classifiers on various sub-samples of the dataset and uses averaging to improve the predictive accuracy and control overfitting reduction in variance
Small increase in bias and loss of interpretability for performance boost
sklearn.ensemble.RandomForestClassifier Parameters:
  N_estimators: number of trees in the forest
  Criterion: function to measure the quality of a split (Gini, Entropy or Log Loss)
  Max_depth: maximum depth of the tree
  Random_state: controls randomness of the bootstrapping of the samples used when building tree and sampling of the features to consider when looking for the best split at each node

## Slide 7: Methods and results - Random Forest

## Slide 8: What we do with rnn and what we get
Simple RNN
  Layers, Learning Rate, Batch Size, Optimizer……
Add Ensemble
  Models Vote to Get the Final Prediction
Use Meta Model
  Model Makes Final Prediction Based on the Base Models’ Prediction
Parameter Tuning

## Slide 9: conclusion and discussion
Why Do Traditional Machine Learning Methods Outperform Neural Networks ?
Why Do These Data Processing Methods Lead to a Decrease in Model Performance ?
  Data Augmentation
  Anomaly Detection
  Shuffle Data
  One-Hot Encoding
What We Found in Feature Engineering ?

## Slide 10: Thank you!